## Slide 1: Panel assembly and plans
Hubert van Hecke
Los Alamos

## Slide 2: 50 cm prototype layout
x
50 cm
4 layers, 2 pairs separated by 5 cm
Element size decreases toward center plane
5 cm

## Slide 3: 16-bar units
5mm

## Slide 4: .
Assemble 16 50-cm bars, hold with blue clamps
Apply stripes of glue
Remove blue clamps
Laser-cut into blocks
Enough to construct
4 50 x 50 cm layers

## Slide 5: Assembly tray
~50 x 50 cm tray printed in 9 sections
Fibers pass under bridges
4mm grooves every 5mm to hold
4 1-mm fibers

## Slide 6: Assembly frame
3mm carbon-fiber-honeycomb sheet
Tray glued to carbon
80-20 Aluminum frame
Carbon honeycomb
Cover sheet

## Slide 7: Fiber couplers
At Fermilab, we saw these couplers:
18 1mm fibers
35 mm wide (<50)
Polished face
Mock them up, and design holders
Outgoing fiber side
WLS
in
Clear
out
Here, all WLS fibers come in on the bottom

## Slide 8: Modify last 3 holders
A
B
C
D
E
F
Fibers from connectors A, B, C go low
Fibers from D, E, F go high

## Slide 9: Test assembly

## Slide 10: Moving connectors closer
.
With new holders, vertical bends are gentle,
And we can move them closer to the tray
But then there is a bad horizontal bend
Modify the last connector holder to give
These fibers more room
Now connectors can be pushed all the way
Against the tray – minimal space used (12 cm)

## Slide 11: 4 layer close fit
5 cm

## Slide 12: On the readout end
2 x 16 clear fibers
4 x 4 mm
SIPMs
Connector holder block
matches PC board
Design by Arielle Platero

## Slide 13: How to install?
Y-shaped brackets (red) hold
pairs of rails (green)
Fiber routing, cable trays

## Slide 14: Next
Is there enough light to read out with 1/2mm fibers?
    Yield down by 4, probably enough
    1/2mm fibers are much more flexible – ease of installation
Obtain connectors
    Depends on (1)
3D print or injection-mold components
    Quantities are small (48 for some, 144 for others) for this prototype
    Printing can keep up with assembly
Go from to
    Needed for the 1-meter version
    Simplify construction

## Slide 15: backup

## Slide 16
Mount point

## Slide 17: Ease of construction
8 fibers, >5mm
4 fibers <5mm

## Slide 18: end