## Slide 1: Physics Impact of MPC-EX on other Subsystems
Oleg Eyser
UCR/BNL
MPC-EX Internal Review
December 9, 2011

## Slide 2: Geometry & Physics
GEANT4
  complete south muon arm + central magnet
QGSP_BERT_HP interactions
  process modeling for neutron thermalization
  complete isotope mix for materials
PYTHIA input  neutron flux or photons

## Slide 3: Thermal Neutrons
Origins of neutrons in MuTr St1
Thermal neutrons behave gas-like
Thermalization happens primarily on hydrogen (water, plastic, G10)

## Slide 4: Inclusion of Pre-Shower
Neutron origins are shifted into the pre-shower
Spallation products are directed (dep. on material)
MuTr St1
MPC read-out

## Slide 5: Slow Neutrons with MPC-EX
Comparison with dedicated Li absorber shows that neutrons leave piston hole before thermalization
It is not important where the neutrons are produced (for a thin component in front of piston hole)
(absorption resonance in W)
per event per cm2

## Slide 6: Fast Neutrons with MPC-EX
Impact on MuTr is comparable to slow neutrons
Increased impact on MPC (read-out and crystals)
Total spectrum falls exponentially

## Slide 7: Summary
Tungsten itself is a pretty good neutron absorber
The directed spallation process leads to an increased neutron flux on the MPC read-out

## Slide 8: Conclusions
Muon Trackers
  High energy gamma emission from thermal neutron capture
  Increased by about 5%
MPC
  Fast neutron background in read-out
  Total neutron flux in PbWO4 crystals
  Increased by about 40%
  Comparable to increased c.o.m. energy 200  500 GeV

## Slide 9: backup

## Slide 10: Single Bunch Analysis Run10
Collision bunch
5ms
15ms
15ms
4ms
9ms
9ms
S.St1
S.St2
S.St3
N.St1
N.St2
N.St3
Tsutomu Mibe

## Slide 11: Thermal Neutron Times
Different regions with changing behavior
Thermalization
Carbon: 110 collisions
Iron: 500 collisions
Lead: 1800 collisions
Effective thermalization takes ≈30 µs
Travel times between stations > 0.5 ms
Very consistent between St1 and St3
thermalization in G10 @ St3
thermalization in G10 @ St1

## Slide 12: Li Absorber in Piston Hole
Absorber in piston hole only has small effect
Additional Li2CO3 absorber at the opening of the piston hole
Using all UIUC Li2CO3
22.0 cm radius
1.2 cm thickness

## Slide 13: Neutron Capture in Tungsten